RAIN MASTER® SENTAR II

Automatic controller(s) shall be the RME SENTAR II Series with stations 6, 12, 18 ,24, 30 or 36 as manufactured under the brand name Irritrol and installed according to the manufactured published specifications and applicable electrical codes.

Operation: Flow Sensing allows for total flow control and break detection (requires flow sensor), Cycle and Soak to eliminate runoff and conserve water and four (4) completely independent programs with five (5) start times, for a total of 20 possible start times per day. Watering times shall allow each station to be set from 1 minute to 9 hrs 59 minutes in 1 minute increments. “Quick Stations” to allow rapid programming of a block of stations with the same watering time and Water Days for each program based on a seven day week or a skip-by-day routine allowing a program to skip from 1 to 30 days between watering. Programmable rain shut down to allow the selection of the number of days the controller will stay off (in rain shut down mode) before it goes back into the automatic mode. A “real time” clock to hold the actual time during power outages without batteries. A non-volatile memory shall hold the program(s) indefinitely during power outages or seasonal shutdown. The Review feature brings all the information for a given program (s) to the displays with simple push of the Review Button. Multiple displays shall provide a simple way of programming and information recall. A manually activated system check/syringe cycle shall sequentially run stations for a user selectable time from 1 minute to 9 minutes. A manually activated program cycle shall run a program independent of its programmed start time and water days. A manually activated station cycle shall run a single station for a selected time. A built-in remote control jack shall be compatible with Rain Master Remotes. Automatic field wire fault detection shall enable the controller to sense a short in the field wire and instantly turn off that station, report the fault and move to the next programmed station. A Rain Switch (auto-off) shall turn off all stations without disturbing the program(s). A percentage key shall allow the user to increase or decrease all station run times on a percentage basis in 1% increments from 0% to 300% by program.

Construction:

• Heavy-duty 18-gauge jet coat, powder coated steel enclosure for outdoor or indoor use.

• Two convenient sized enclosures for easy installation of field wires.

• Outdoor pedestal mount available for all models.

• Comes with a limited 5-year warranty.

Electric:

• Models are available for 120V ac, 50/60 Hz or 220/240 V ac 50/60 Hz power.

• Extra heavy--duty lightning and surge-protected models available for 	   areas where lightning is a concern.

• UL and C-UL listed

Setup Operation:

The following features can be easily selected or reconfigured by a single push of a button (SETUP key):

• Programmable master valve/pump allows the master valve or pump to go on by program.

• Programmable stacking or no stacking of programs selects programs to  run one after the other (Stack Mode) or at the same time (No Stack Mode).

• Programmable timer delay between stations establishes a time delay  from 1 second to 256 seconds (4 minutes 16 seconds) to allow slow-closing valves to completely shut off.

• Programmable security code allows entry of a 1 - 4 digit number as a security code to prevent access by unauthorized personnel.

• Programmable sensor to enable or disable sensor operation for each program.

• Programmable alarm to either enable or disable an audible alarm in the event of a field wire fault.

Electrical Specifications:

• Input power required: 105-130 V ac, 50/60 Hz, .5 amp maximum, .1 amp idle

• Output power: 24 V ac, 1.5 amps maximum total output (36VA) 1 amp