Bidding Specifications

The STEALTH kit is a turf cup installed onto any INFINITY sprinkler that allows natural turf growth atop the sprinkler.  Having natural turf on top of the hard plastic sprinkler case prevents a significant unnatural bounce should a golf ball strike it, improves the landscapes natural beauty and prevents potential trip hazards.

The kit shall consist of the following components:

- Turf Cup – The turf cup shall be injection molded from Urethane, a flexible and durable engineering plastic. The turf cup and cover rubber are designed to seal against one another when completely retracted and flush during pop-up and retraction to prevent debris contamination and potential stick-ups.  The turf cup shall provide access to the TruJectory adjuster through a cross slit raised tubular feature that is .25” below grade.  The location of the raised tubular feature shall be identified by a raised boss on the inner edge of the turf cup.

- Support, turf cup – The support shall be an injection molded part from ABS to ensure the position and stability of the turf cup.  It shall have through holes to promote drainage and prevent root rot and to allow root binding for support of the turf.

- Rubber Cover – The rubber cover shall be injection molded from Urethane, a flexible and durable engineering plastic. The rubber cover and turf cup are designed to seal against one another when completely retracted and flush during pop-up and retraction to prevent debris contamination and potential stick-ups. The rubber cover shall incorporate slots to promote drainage from the turf cup and access to the manual selector through a cross slit raised tubular feature .25” below grade .   The location of the raised tubular feature shall be identified by a raised boss on the outer edge of the cover, rubber.

- Support, cover -  The support shall be an injection molded part from ABS to ensure the position and stability of the rubber cover.

- Screw, cover – Three longer screws to secure the rubber cover, support and existing cover.  Screws shall incorporate a hex head to allow for ease of removal with soil present.

- Screw, cap – One longer screw to secure the turf cup, support and existing cap.

- Plug, nozzle – A slot nozzle plug shall be provided in the STEALTH-T kit to plug the molded in slot nozzle and eliminate excess water around the head   With the sprinkler now 2” lower, the slot nozzle may cause excess water around the sprinkler.  Placing the plug into the slot will prevent this.

All Toro sprinklers allow adjustment of the inner nozzle to reduce the in-close water.  The Stealth kit installation moves the sprinkler 2” lower making this adjustability extremely valuable in preventing excessive water around the sprinkler.  The instructions provided with each kit shall provide inner nozzle adjustment instructions.